## Slide 1: A Design of a Complete Network Communication System (L1&L2)
Southern University of Science and Technology
Xiwen Huang
Team GUOLAIBU
EEE, SUSTech

## Slide 2: Why Communication?
Southern University of Science and Technology
Host B requires data from host A for its own application.

## Slide 3: We need to build a network communication system!
Southern University of Science and Technology
To enable communication,

## Slide 4: Simplest Case: Point-to-Point (P2P)
Southern University of Science and Technology
No network layer and above.
No host identifying, no addressing, routing or forwarding.
No src and dst headers in frame building.
Focus on physical and link layer:
Digital signal generation, modulation, transmission, demodulation, data recovery.
Longer message (fragmentation), error detection.

## Slide 5: P2P: Digital signal generation & data recovery
Southern University of Science and Technology
One-to-one correspondence (UTF-8).
Eg: “我”——“1101” (Just a demonstration, not accurate.)

## Slide 6: P2P: Modulation (Digital to Analog)
Southern University of Science and Technology
ASK (Amplitude Shift Keying)
Change 1/0 to samples of sine functions.

## Slide 7: P2P: Modulation (Digital to Analog)
Southern University of Science and Technology
Our design:
A0 = 0.1
A1 = 1.0

## Slide 8: P2P: Transmission
Southern University of Science and Technology
Analog
Attenuation, noise (which may cause bit error)
Propagation delay

## Slide 9: P2P: Transmission
Southern University of Science and Technology

## Slide 10: P2P: Transmission (Performance Analysis)
Southern University of Science and Technology

## Slide 11: P2P: Demodulation (Analog to Digital)
Southern University of Science and Technology
Threshold: (= 0.3 in our design)

## Slide 12: P2P: Result
Southern University of Science and Technology

## Slide 13: P2P: Longer message
Southern University of Science and Technology
The sender splits a long message into multiple fragments of a fixed size (64 bytes). Each fragment is prefixed with a 6-byte header consisting of: message_id (2 bytes, an identifier for the message), fragment_index (2 bytes, the index of this fragment), and total (2 bytes, the total number of fragments). Each fragment is then individually encapsulated into a frame and transmitted over the physical channel.
On the receiver side, a reassembly buffer is created based on message_id. As fragments arrive, they are inserted into a dictionary according to their fragment_index. When all total fragments have been received, the receiver concatenates (连接) them in order to reconstruct the complete byte sequence, then decodes it using UTF-8 to recover the original message.

## Slide 14: P2P: Longer message
Southern University of Science and Technology

## Slide 15: P2P: Error detection
Southern University of Science and Technology
Parity check
Byte -- 8 bits a block:
For even number of 1s: add 0 as the parity bit
For odd number of 1s: add 1 as the parity bit
Finally, payload + parity have an even number of 1s in total. (1)
Receiver: Check if (1) is true. (Also check if the length of total bits is multiples of nine.)

## Slide 16: P2P: Error detection
Southern University of Science and Technology
Change Threshold to 0.05:

## Slide 17: Multi-host System
Southern University of Science and Technology
Design 1
No scalability
Design 2
Scalable

## Slide 18: Multi-host: Router
Southern University of Science and Technology

## Slide 19: Multi-host: Workflow
Southern University of Science and Technology

## Slide 20: Multi-host: Result
Southern University of Science and Technology

## Slide 21: Multi-host: Result
Southern University of Science and Technology

## Slide 22: Multi-host: Result
Southern University of Science and Technology

## Slide 23: Multi-host: Result (simultaneous transmission)
Southern University of Science and Technology

## Slide 24: Multi-host: Result (simultaneous transmission)
Southern University of Science and Technology

## Slide 25: Thank You!
Southern University of Science and Technology
I am open to any questions you may have.